## Slide 1
SMART SAFETY SYSTEM
An IoT based gas, flame and heat detector with remote control
Detects on the device. Reports to the cloud. Controlled from a phone.
Bahçeşehir University · Faculty of Engineering and Natural Sciences
Department of Computer Engineering · CMP3010 Embedded Systems Programming
Ege Gürtünca · 2202775
Notes: Smart Safety System. Gas, flame and heat detection that keeps working without the internet, and can be watched and controlled from an Android app.

## Slide 2
01 · MOTIVATION
The Problem & The Approach
1
It only beeps in that room
A normal detector makes a sound where it is installed. If nobody is home, nobody hears it.
2
Smart ones are expensive and closed
They cost much more, depend on the maker's cloud, and cannot be repaired or extended.
3
No record of what happened
You cannot go back and see when the gas level rose or how long the alarm lasted.
THE APPROACH
All detection and the fan run on the Arduino.
The Arduino never waits for the network.
Wi-Fi only adds reporting and a few commands.
If the internet dies, the detector still works.
Notes: Ordinary detectors are local only. Smart ones are costly and closed. My design keeps the safety logic on the device and treats the cloud as an extra, not a dependency.

## Slide 3
02 · WHAT IT DOES
Three Capabilities
1
Sense
Gas and smoke with an MQ-2
Flame with an infrared sensor
Temperature and humidity with a DHT11
2
React
12 V fan through a relay
Buzzer and red / green LEDs
Live values on a 16x2 LCD
3
Report & Control
Readings to a Flask server every 5 s
Charts and alarm log in an Android app
Fan, mute and thresholds set remotely
The alarm decision is made only on the Arduino, not in the app or on the server.
Notes: Three groups: sensing, local reaction, and remote reporting with control. The important part is that the decision lives on the Arduino.

## Slide 4
03 · HARDWARE
Components & Sensors
Arduino Uno
Sensors, alarm, relay, LCD
NodeMCU ESP8266
Wi-Fi gateway, carries data only
MQ-2
LPG, methane and smoke
IR flame sensor
Open flame
DHT11
Temperature and humidity
Relay + 12 V fan
Emergency ventilation
Buzzer + 2 LEDs
Audible and visual alarm
16x2 I2C LCD
Local readout, two pins
microSD module
Local log every 2 s
8 x AA pack
Separate 12 V for the fan
Most boards and sensors came from the lab stock. I bought the LCD, the fan, the battery pack, the LEDs, the buttons, the resistors and the jumper wires.
Notes: Ten parts. The Arduino runs the safety logic, the NodeMCU is only a gateway. The fan runs on its own 12 V pack so it never loads the 5 V logic.

## Slide 5
04 · ARCHITECTURE
System Design
Sensors
MQ-2, flame, DHT11
Arduino Uno
Decides the alarm. Drives fan, buzzer, LEDs, LCD and SD.
NodeMCU
Wi-Fi and HTTPS. Carries data only.
Flask on Render
Stores in Supabase. Answers with the command.
Android app and web
Live values, charts, alarm log, controls.
Data goes up
Arduino to NodeMCU every second, NodeMCU to the server every five seconds as an 88 byte JSON message.
Commands come back down
The server puts the command inside its answer to the same POST, so a command arrives within five seconds.
Notes: Data flows left to right. Commands ride back on the response of the measurement POST, so there is no MQTT, no second endpoint and no extra polling loop.

## Slide 6
05 · DETECTION LOGIC
When Does It Alarm?
Gas
MQ-2 reading
≥ 400
Flame
IR reading
≤ 80
Fast heating
+5 °C within
60 seconds
Absolute heat
Temperature
≥ 45 °C
Why two heat rules?
A fire shows itself as a fast rise, not as a high number. An absolute limit alone gives false alarms in summer and reacts too late in winter, so the device keeps a 60 second window of samples and watches both.
Humidity is a warning, not an alarm
Above 80 % or below 25 % the LCD alternates every two seconds between the readings and the warning. The fan, the buzzer and the relay are not touched. All thresholds can be changed from the phone.
Notes: Four alarm conditions and one warning. Every threshold is adjustable from the app and stored in EEPROM.

## Slide 7
06 · SAFETY DESIGN
Three Rules Kept in the Firmware
1
Remote control can only turn the fan ON
You cannot switch the fan off from the phone while there is a gas alarm.
fanOn = alarm OR button OR remote
2
Mute clears itself
Otherwise one press would silence the system forever.
server resets mute when alarm ends
3
Thresholds live in EEPROM
They survive a power cut, and the 100k write limit is respected.
written only when a value changes
All three are enforced on the Arduino, so a bug in the app or the server cannot break them.
Notes: These three rules are the reason the system is a safety device and not a remote control. They are all in the firmware.

## Slide 8
07 · WHAT WENT WRONG
Technical Challenges & Solutions
PROBLEM
SOLUTION
Commands arrived broken
SoftwareSerial cannot send and receive at the same time, so two commands stuck together.
Added an XOR checksum. A line that does not match is thrown away; the next one arrives in five seconds.
The Uno ran out of RAM
80 % used. The LCD stayed blank and the EEPROM values turned into garbage.
Wrapped every string in the F() macro so it stays in flash. RAM use dropped to 64 %.
One bad reading lost everything
When the DHT11 failed it sent nan, the JSON became invalid and the whole POST was rejected.
Values that are not numbers are sent as null, so gas and flame still reach the server.
A dead device looked safe
If the device stopped sending, the last reading stayed on screen and everything looked normal.
The server reports the age of the reading. Older than 60 seconds and the app warns instead of showing NORMAL.
Notes: Four real problems. The last one matters most: a dead device that still looks safe is the most dangerous failure mode of a safety system.

## Slide 9
08 · VERIFICATION
Testing & Verified Results
Specification | Target | How I tested it
Gas and flame detection speed | Under 1 second | Timestamps in the serial monitor
Local reaction to an alarm | Fan, buzzer and LED | Lighter near the flame sensor
Data reaching the server | Every 5 seconds | created_at values in the database
Command round trip | 5 seconds or less | Button press to CMD line in the log
Thresholds survive a power cut | Yes | Unplugged the board, read them at boot
Broken commands rejected | All of them | Five different corrupted lines
Noticing a silent device | 60 seconds or less | Record age reported by the server
Free RAM on the Arduino | Above 25 % | Compiler output after uploading
Every specification was checked on the built system, not on paper.
Notes: Eight specifications, each with a target and the way I measured it.

## Slide 10
09 · PHOTOS
The Built System
Finished case, LCD showing live values
Inside: Arduino, breadboard, relay, NodeMCU
Running with the case open
Wiring and the 12 V battery pack
The case is a cardboard box covered in foil, with the LCD, the two LEDs and the button on the front and the fan on the side.
Notes: The green LED means no alarm. The LCD alternates between the readings and the humidity warning when humidity is out of range.

## Slide 11
10 · PROJECT PLAN
Timeline & Cost
3
Week 3
Proposal, design, ordering the parts
4
Week 4
Sensors, Arduino and NodeMCU firmware, server
5
Week 5
Web page, Android app, command channel
6
Week 6
Testing, fixes and the report
7
Week 7
Presentation
The term started on 27 July 2026. I worked alone, so the work was split into stages instead of people.
545.59 TL
what I actually paid — the lab supplied the boards and the sensors
≈ 1350 TL
to build the whole system from scratch
0 TL
server, database and notifications — every service on a free plan
Notes: The project cost me 545 lira because the lab supplied the boards and sensors. Running it costs nothing.

## Slide 12
11 · WHAT COMES NEXT
Future Work
Wi-Fi reconnect and a watchdog
The NodeMCU does not reconnect by itself after the network drops, and neither board has a watchdog timer yet.
Hysteresis on the relay
A reading sitting exactly on the threshold makes the fan switch on and off repeatedly.
Calibrating the MQ-2
The gas threshold is a sensible default. It has not been calibrated against a known gas concentration.
A better sensor set
A DHT22 measures up to 80 °C, which would make the heat alarm useful in a real fire.
The prototype works on a breadboard. It is not a certified detector and I would not tell anyone to use it instead of one.
Notes: Known limits, stated honestly. The most important one is that the NodeMCU does not reconnect after a Wi-Fi drop.

## Slide 13
APPENDIX · SOURCE CODE
Arduino Firmware (1/3)
sketch_aug13a.ino
Notes: Arduino Firmware, part 1 of 3.

## Slide 14
APPENDIX · SOURCE CODE
Arduino Firmware (2/3)
sketch_aug13a.ino
Notes: Arduino Firmware, part 2 of 3.

## Slide 15
APPENDIX · SOURCE CODE
Arduino Firmware (3/3)
sketch_aug13a.ino
Notes: Arduino Firmware, part 3 of 3.

## Slide 16
APPENDIX · SOURCE CODE
NodeMCU Firmware (1/3)
sketch_aug13b.ino
Notes: NodeMCU Firmware, part 1 of 3.

## Slide 17
APPENDIX · SOURCE CODE
NodeMCU Firmware (2/3)
sketch_aug13b.ino
Notes: NodeMCU Firmware, part 2 of 3.

## Slide 18
APPENDIX · SOURCE CODE
NodeMCU Firmware (3/3)
sketch_aug13b.ino
Notes: NodeMCU Firmware, part 3 of 3.

## Slide 19
References
Arduino
Arduino Uno Rev3 Documentation
docs.arduino.cc/hardware/uno-rev3
Hanwei Electronics
MQ-2 Semiconductor Sensor for Combustible Gas
pololu.com/file/download/MQ2.pdf
Aosong Electronics
DHT11 Humidity and Temperature Sensor
mouser.com/datasheet/2/758
Espressif Systems, 2023
ESP8266EX Datasheet, version 6.9
espressif.com · esp8266ex_datasheet_en.pdf
NFPA, 2022
NFPA 72 National Fire Alarm and Signaling Code
Rate of rise heat detectors
CEN, 2018
EN 50291-1 Detection of carbon monoxide in premises
Brussels
Thank you
Notes: Thank you. Happy to answer questions.